## Slide 1
Topic 3
Cores and Wrappers

## Slide 2: Hardware Cores and Models
8.1 Synthesis Rules and Styles
8.1.1 Combinational Cores
8.1.2 Sequential Cores
8.1.3 Finite State Machines
8.2 Memory and Queue Structures
8.2.1 Generic RAM Core
8.2.2 Synthesizable Push-Pop Stack
8.2.3 Synthesizable Circular FIFO

## Slide 3: Hardware Cores and Models
8.3 Arithmetic Cores
8.3.1 Array Multiplier
8.3.2 Carry-Lookahead Adder
8.3.3 Synthesizable Booth Multiplier
8.4 Components with Separate Control and Data Parts
8.4.1 Sequential Multiplier
8.4.2 von Neumann Computer Model
8.5 Summary

## Slide 4: Synthesis Rules and Styles
Synthesis
Rules and Styles
Combinational
Cores
Sequential
Cores
Finite State
Machines

## Slide 5: Combinational Cores
Synthesis
Rules and Styles
Combinational
Cores
Sequential
Cores
Finite State
Machines
Combinational
Cores

## Slide 6: Combinational Cores
Describing combinational circuits:
  Concurrent Assignments
  Sequential Bodies
  Component Instantiations

## Slide 7: Combinational Cores
Combinational
Cores
Concurrent
Assignments
Combinational
Process
Statements
Process
Combinational
Style
Instantiation
of other
Components

## Slide 8: Concurrent Assignments
Combinational
Cores
Concurrent
Assignments
Combinational
Process
Statements
Process
Combinational
Style
Instantiation
of other
Components
Concurrent
Assignments

## Slide 9: Concurrent Assignments
Various forms of concurrent signal assignments :
  Simple Assignments
  Conditional Assignments
  Selected Signal Assignments

## Slide 10: Concurrent Assignments
LIBRARY IEEE;
USE IEEE.std_logic_1164.ALL;
USE IEEE.std_logic_unsigned.ALL;
ENTITY comparator IS
PORT (a, b: IN std_logic_vector;
gt, eq, lt: OUT std_logic);
END ENTITY comparator;
--
ARCHITECTURE expression OF comparator IS
BEGIN
eq <= '1' WHEN (a=b) ELSE '0';
gt <= '1' WHEN (a>b) ELSE '0';
lt <= '1' WHEN (a<b) ELSE '0';
END ARCHITECTURE expression;
Synthesizable Magnitude Comparator

## Slide 11: Concurrent Assignments
ENTITY comparator IS
PORT (a, b: IN std_logic_vector;
gt, eq, lt: OUT std_logic);
BEGIN
ASSERT a'LENGTH = b'LENGTH
REPORT comparator'PATH_NAME & ". Operand size
mismatch";
END ENTITY comparator;
Entity Declaration with Assertion

## Slide 12: Combinational Process Statements
Combinational
Cores
Concurrent
Assignments
Combinational
Process
Statements
Process
Combinational
Style
Instantiation
of other
Components
Combinational
Process
Statements

## Slide 13: Combinational Process Statements
LIBRARY IEEE;
USE IEEE.std_logic_1164.ALL;
USE IEEE.std_logic_unsigned.ALL;
ENTITY alu IS
PORT (a, b : IN std_logic_vector;
add_sub : IN std_logic;
func : IN std_logic_vector (1 DOWNTO 0);
y : OUT std_logic_vector;
gt, eq, lt, co : OUT std_logic);
END ENTITY;
--
. . . . . . . . . . . . . .
Mixed Level ALU

## Slide 14: Combinational Process Statements
ARCHITECTURE procedural OF alu IS
SIGNAL result : std_logic_vector (a'LENGTH DOWNTO 0);
BEGIN
PROCESS (a, b, add_sub, func) BEGIN
CASE func IS
WHEN "00" =>
IF (add_sub = '1') THEN
result <= ('0'&a) - ('0'&b);
ELSE
result <= ('0'&a) + ('0'&b);
END IF;
WHEN "01" => result <= '0'&a;
WHEN "10" => result <= ('0'&a) AND ('0'&b);
WHEN "11" => result <= NOT '1'&a;
WHEN OTHERS => result <= (OTHERS => '0');
END CASE;
Mixed Level ALU (Continued)

## Slide 15: Combinational Process Statements
. . . . . . . . . . . . . .
. . . . . . . . . . . . . .
UUT1: ENTITY WORK.compartor(expression)
PORT MAP (a, b, gt, eq, lt);
y <= result (a'LENGTH - 1 DOWNTO 0);
co <= result (result'LEFT);
END ARCHITECTURE procedural;
Mixed Level ALU (Continued)

## Slide 16: Process Combinational Style
Combinational
Cores
Concurrent
Assignments
Combinational
Process
Statements
Process
Combinational
Style
Instantiation
of other
Components
Process
Combinational
Style

## Slide 17: Process Combinational Style
ARCHITECTURE procedural OF alu IS
SIGNAL result : std_logic_vector (a'LENGTH DOWNTO 0);
BEGIN
PROCESS (a, b, add_sub, func) BEGIN
CASE func IS
WHEN "00" =>
IF (add_sub = '1') THEN
result <= ('0'&a) - ('0'&b);
ELSE
result <= ('0'&a) + ('0'&b);
END IF;
WHEN "01" => result <= '0'&a;
WHEN "10" => result <= ('0'&a) AND ('0'&b);
WHEN "11" => result <= NOT '1'&a;
WHEN OTHERS => result <= (OTHERS => '0');
END CASE;
Mixed Level ALU (Continued)
RULE 1

## Slide 18: Process Combinational Style
ARCHITECTURE procedural OF alu IS
SIGNAL result : std_logic_vector (a'LENGTH DOWNTO 0);
BEGIN
PROCESS (a, b, add_sub, func) BEGIN
CASE func IS
WHEN "00" =>
IF (add_sub = '1') THEN
result <= ('0'&a) - ('0'&b);
ELSE
result <= ('0'&a) + ('0'&b);
END IF;
WHEN "01" => result <= '0'&a;
WHEN "10" => result <= ('0'&a) AND ('0'&b);
WHEN "11" => result <= NOT '1'&a;
WHEN OTHERS => result <= (OTHERS => '0');
END CASE;
Mixed Level ALU (Continued)
RULE 2

## Slide 19: Process Combinational Style
PROCESS (a, b, add_sub, func) BEGIN
result <= (result'RANGE => '0');
CASE func IS
WHEN "00" =>
IF (add_sub = '1') THEN
result <= ('0'&a) - ('0'&b);
ELSE
result <= ('0'&a) + ('0'&b);
END IF;
WHEN "01" => result (7 DOWNTO 0) <= a;
WHEN "10" => result (7 DOWNTO 0) <= a AND b;
WHEN "11" => result (7 DOWNTO 0) <= NOT a;
WHEN OTHERS => result <= (OTHERS => '0');
END CASE;
END PROCESS;
Inactive Process Output Setting
RULE 2

## Slide 20: Instantiation of Other Components
Combinational
Cores
Concurrent
Assignments
Combinational
Process
Statements
Process
Combinational
Style
Instantiation
of other
Components
Instantiation
Of other
Components

## Slide 21: Instantiation of Other Components
. . . . . . . . . . . . . .
. . . . . . . . . . . . . .
UUT1: ENTITY WORK.compartor(expression)
PORT MAP (a, b, gt, eq, lt);
y <= result (a'LENGTH - 1 DOWNTO 0);
co <= result (result'LEFT);
END ARCHITECTURE procedural;
Mixed Level ALU (Continued)

## Slide 22: Sequential Cores
Synthesis
Rules and Styles
Combinational
Cores
Sequential
Cores
Finite State
Machines
Sequential
Cores

## Slide 23: Sequential Cores
Sequential
Cores
Using
Block
Statements
Process Statement
for
Sequential Logic
Asynchronous
Control
Process Statement
Sequential
Circuit Synthesis

## Slide 24: Using Block Statements
Sequential
Cores
Using
Block
Statements
Process Statement
for
Sequential Logic
Asynchronous
Control
Process Statement
Sequential
Circuit Synthesis
Using
Block
Statements

## Slide 25: Using Block Statements
LIBRARY IEEE;
USE IEEE.std_logic_1164.ALL;
USE IEEE.std_logic_unsigned.ALL;
ENTITY counter IS
PORT (clk, cen, rst, u_d : IN std_logic;
q : OUT std_logic_vector);
END ENTITY ;
. . . . . . . . . . . . . .
Counter Using Block Statements

## Slide 26: Using Block Statements
ARCHITECTURE blockbased OF counter IS
SIGNAL cnt_reg : std_logic_vector(q'RANGE) REGISTER;
BEGIN
cl: BLOCK (clk = '1' AND NOT clk'STABLE) BEGIN
en: BLOCK ((cen = '1' AND GUARD) OR rst = '1') BEGIN
cnt_reg <= GUARDED
(cnt_reg'RANGE => '0') WHEN rst = '1' ELSE
cnt_reg + 1 WHEN u_d = '1' ELSE
cnt_reg - 1;
END BLOCK;
END BLOCK;
q <= cnt_reg;
END ARCHITECTURE;
Counter Using Block Statements (Continued)

## Slide 27: Process Statement for Sequential Logic
Sequential
Cores
Using
Block
Statements
Process Statement
for
Sequential Logic
Asynchronous
Control
Process Statement
Sequential
Circuit Synthesis
Process Statement
for
Sequential Logic

## Slide 28: Process Statement for Sequential Logic
LIBRARY IEEE;
USE IEEE.std_logic_1164.ALL;
USE IEEE.std_logic_unsigned.ALL;
ENTITY shift_reg IS
PORT (clk, ld, rst, l_r, shen, s_in, oe :
IN std_logic;
dio : INOUT std_logic_vector);
END ENTITY;
--
Shift-register Using Process Statement

## Slide 29: Process Statement for Sequential Logic
ARCHITECTURE synch OF shift_reg IS
SIGNAL parout : std_logic_vector (dio'RANGE)
:= (OTHERS => '0');
BEGIN
PROCESS (clk)
CONSTANT li : INTEGER := dio'LEFT;
BEGIN
IF (clk = '1' AND clk'EVENT) THEN
IF (rst = '1') THEN
parout <= (OTHERS => '0');
ELSIF (ld = '1') THEN
parout <= dio;
ELSIF (shen = '1') THEN
. . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . .
END ARCHITECTURE synch;
Shift-register Using Process Statement (Continued)

## Slide 30: Process Statement for Sequential Logic
. . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . .
ELSIF (shen = '1') THEN
IF (l_r = '1') THEN
parout <= parout (li-1 DOWNTO 0) & s_in;
ELSE
parout <= s_in & parout (li DOWNTO 1);
END IF;
ELSE
parout <= parout; -- Not needed
END IF;
END IF;
END PROCESS;
dio <= parout WHEN (oe='1') AND (ld='0') ELSE
(dio'RANGE => 'Z');
END ARCHITECTURE synch;
Shift-register Using Process Statement (Continued)

## Slide 31: Asynchronous Control
Sequential
Cores
Using
Block
Statements
Process Statement
for
Sequential Logic
Asynchronous
Control
Process Statement
Sequential
Circuit Synthesis
Asynchronous
Control

## Slide 32: Asynchronous Control
ARCHITECTURE asynch OF shift_reg IS
SIGNAL parout : std_logic_vector (dio'RANGE)
:= (OTHERS => '0');
BEGIN
PROCESS (clk, rst)
CONSTANT li : INTEGER := dio'LEFT;
BEGIN
IF (rst = '1') THEN
parout <= (OTHERS => '0');
ELSIF (clk = '1' AND clk'EVENT) THEN
IF (ld = '1') THEN
parout <= dio;
. . . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . . .
END PROCESS;
dio <= parout WHEN (oe='1') AND (ld='0') ELSE
(dio'RANGE => 'Z');
END ARCHITECTURE asynch;

## Slide 33: Process Statement Sequential Circuit Synthesis
Sequential
Cores
Using
Block
Statements
Process Statement
for
Sequential Logic
Asynchronous
Control
Process Statement
Sequential
Circuit Synthesis
Process Statement
Sequential
Circuit Synthesis

## Slide 34: Finite State Machines
Synthesis
Rules and Styles
Combinational
Cores
Sequential
Cores
Finite State
Machines
Finite State
Machines

## Slide 35: Finite State Machines
Finite State
Machines
Moore
Machines
Mealy
Machines
Huffman
Coding Style
A More Modular
State Machine
Coding Style

## Slide 36: Moore Machines
Finite State
Machines
Moore
Machines
Mealy
Machines
Huffman
Coding Style
A More Modular
State Machine
Coding Style
Moore
Machines

## Slide 37: Moore Machines
A Moore 101 Detector

## Slide 38: Moore Machines
ENTITY moore_detector IS
PORT (x, rst, clk : IN std_logic; z : OUT std_logic);
END ENTITY ;
ARCHITECTURE procedural OF moore_detector IS
TYPE state IS (reset, got1, got10, got101);
SIGNAL current : state := reset;
BEGIN
PROCESS (clk) BEGIN
IF (clk = '1' AND clk'EVENT) THEN
IF rst = '1' THEN
current <= reset;
. . . . . . . . . . . . . . . .
    END IF;
END PROCESS;
z <= '1' WHEN current = got101 ELSE '0';
END ARCHITECTURE;
Moore Machine VHDL Code

## Slide 39: Moore Machines
ELSE
CASE current IS
WHEN reset =>
IF x = '1' THEN current <= got1;
ELSE current <= reset; END IF;
WHEN got1 =>
IF x = '0' THEN current <= got10;
ELSE current <= got1; END IF;
WHEN got10 =>
IF x = '1' THEN current <= got101;
ELSE current <= reset; END IF;
WHEN got101 =>
IF x = '1' THEN current <= got1;
ELSE current <= got10; END IF;
WHEN OTHERS => current <= reset;
END CASE;
Moore Machine VHDL Code (Continued)

## Slide 40: Moore Machines
. . . . . . . . . . . . . .
END IF;
END IF;
END PROCESS;
z <= '1' WHEN current = got101 ELSE '0';
END ARCHITECTURE;
Moore Machine VHDL Code (Continued)

## Slide 41: Moore Machines
VHDL Code Correspondence with the got10 State

## Slide 42: Mealy Machines
Finite State
Machines
Moore
Machines
Mealy
Machines
Huffman
Coding Style
A More Modular
State Machine
Coding Style
Mealy
Machines

## Slide 43: Mealy Machines
A 101 Mealy Machine

## Slide 44: Mealy Machines
ENTITY mealy_detector2 IS
PORT (x, clk, rst : IN std_logic; z : OUT std_logic);
END ENTITY mealy_detector2;
--
ARCHITECTURE procedural OF mealy_detector2 IS
TYPE state IS (reset, got1, got10);
SIGNAL current : state := reset;
BEGIN
PROCESS (clk, rst) BEGIN
. . . . . . . . . . . . . . . . . . .
END PROCESS;
z <= '1' WHEN (current = got10 AND x = '1') ELSE '0';
END ARCHITECTURE;
Mealy Machine VHDL Code

## Slide 45: Mealy Machines
PROCESS (clk, rst) BEGIN
IF rst = '1' THEN
current <= reset;
ELSIF (clk = '1' AND clk'EVENT) THEN
CASE current IS
WHEN reset =>
IF x = '1' THEN current <= got1;
ELSE current <= reset; END IF;
WHEN got1 =>
IF x = '1' THEN current <= got1;
ELSE current <= got10; END IF;
WHEN got10 =>
IF x = '1' THEN current <= got1;
ELSE current <= reset; END IF;
WHEN OTHERS => current <= reset;
END CASE;
END IF;
END PROCESS;

## Slide 46: Mealy Machines
Mealy State and Output Coding

## Slide 47: Huffman Coding Style
Finite State
Machines
Moore
Machines
Mealy
Machines
Huffman
Coding Style
A More Modular
State Machine
Coding Style
Huffman
Coding Style

## Slide 48: Huffman Coding Style
Huffman Style of Coding a State Machine

## Slide 49: Huffman Coding Style
ENTITY moore_detector4 IS
PORT (x, rst, clk : IN std_logic; z : OUT std_logic);
END ENTITY ;
--
ARCHITECTURE procedural OF moore_detector4 IS
TYPE state IS (reset, got1, got10, got101);
SIGNAL p_state, n_state : state;
BEGIN
combinational: PROCESS (p_state, x) BEGIN
. . . . . . . . . .
END PROCESS combinational;
sequential: PROCESS (clk) BEGIN
. . . . . . . . . .
END PROCESS sequential;
END ARCHITECTURE;
Moore Detector VHDL Code According to Huffman Model

## Slide 50: Huffman Coding Style
combinational: PROCESS (p_state, x) BEGIN
n_state <= reset;
z <= '1';
CASE p_state IS
WHEN reset =>
IF x = '1' THEN n_state <= got1;
ELSE n_state <= reset; END IF;
z <= '0';
WHEN got1 =>
IF x = '0' THEN n_state <= got10;
ELSE n_state <= got1; END IF;
z <= '0';
. . . . . . . . . . . . . . .
END CASE;
END PROCESS combinational;
Moore Detector VHDL Code According to Huffman Model (Continued)

## Slide 51: Huffman Coding Style
combinational: PROCESS (p_state, x) BEGIN
. . . . . . . . . . . . . . . . .
CASE p_state IS
. . . . . . . . . . . . . . . .
WHEN got10 =>
IF x = '1' THEN n_state <= got101;
ELSE n_state <= reset; END IF;
z <= '0';
WHEN got101 =>
IF x = '1' THEN n_state <= got1;
ELSE n_state <= got10; END IF;
z <= '1';
WHEN OTHERS =>
n_state <= reset;
z <= '0';
END CASE;
END PROCESS combinational;
Moore Detector VHDL Code According to Huffman Model

## Slide 52: Huffman Coding Style
sequential: PROCESS (clk) BEGIN
IF (clk = '1' AND clk'EVENT) THEN
IF rst = '1' THEN p_state <= reset;
ELSE
p_state <= n_state;
END IF;
END IF;
END PROCESS sequential;
Moore Detector VHDL Code According to Huffman Model (Continued)

## Slide 53: A More Modular State Machine Coding Style
Finite State
Machines
Moore
Machines
Mealy
Machines
Huffman
Coding Style
A More Modular
State Machine
Coding Style
A More Modular
State Machine
Coding Style

## Slide 54: A More Modular State Machine Coding Style
Using Three Separate Blocks for Describing a State Machine

## Slide 55: A More Modular State Machine Coding Style
ENTITY mealy_detector6 IS
PORT (x, en, clk, rst : IN std_logic;
z : OUT std_logic);
END ENTITY mealy_detector6;
ARCHITECTURE procedural OF mealy_detector6 IS
TYPE state IS (reset, got1, got11, got10);
SIGNAL p_state, n_state : state;
BEGIN
PROCESS (p_state, x) BEGIN
. . . . . . . . . . .
PROCESS (p_state, x) BEGIN
. . . . . . . . . . .
PROCESS (clk) BEGIN
. . . . . . . . . . .
END ARCHITECTURE;
A Mealy Machine Using Three Sequential Processes

## Slide 56: A More Modular State Machine Coding Style
PROCESS (p_state, x) BEGIN
CASE p_state IS
WHEN reset =>
IF x = '1' THEN n_state <= got1;
ELSE n_state <= reset; END IF;
WHEN got1 =>
IF x = '1' THEN n_state <= got11;
ELSE n_state <= got10; END IF;
WHEN got11 =>
IF x = '0' THEN n_state <= got10;
ELSE n_state <= got11; END IF;
WHEN got10 =>
IF x = '1' THEN n_state <= got1;
ELSE n_state <= reset; END IF;
WHEN OTHERS => n_state <= reset;
END CASE;
END PROCESS;

## Slide 57: A More Modular State Machine Coding Style
PROCESS (p_state, x) BEGIN
CASE p_state IS
WHEN reset => z <= '0';
WHEN got1 => z <= '0';
WHEN got11 => IF x = '1' THEN z <= '0';
ELSE z <= '1'; END IF;
WHEN got10 => IF x = '1' THEN z <= '1';
ELSE z <= '0'; END IF;
WHEN OTHERS => z <= '0';
END CASE;
END PROCESS;
A Mealy Machine Using Three Sequential Processes (Continued)

## Slide 58: A More Modular State Machine Coding Style
PROCESS (clk) BEGIN
IF (clk = '1' AND clk'EVENT) THEN
IF rst = '1' THEN p_state <= reset;
ELSE
IF en = '1' THEN
p_state <= n_state;
END IF;
END IF;
END IF;
END PROCESS;
A Mealy Machine Using Three Sequential Processes (Continued)

## Slide 59: Memory and Queue Structures
Memory and
Queue
Structures
Generic
RAM Core
Synthesizable
Push-Pop
Stack
Synthesizable
Circular FIFO
Dynamic
Access Type
FIFO

## Slide 60: Generic RAM Core
Memory and
Queue
Structures
Generic
RAM Core
Synthesizable
Push-Pop
Stack
Synthesizable
Circular FIFO
Dynamic
Access Type
FIFO
Generic
RAM Core

## Slide 61: Generic RAM Core
PROCEDURE init_mem (VARIABLE memory: OUT mem;
CONSTANT datafile: STRING) IS
FILE stddata : TEXT;
VARIABLE l : LINE;
VARIABLE data : std_logic_vector(memory'RANGE(2));
BEGIN
FILE_OPEN (stddata, datafile, READ_MODE);
FOR i IN memory'RANGE(1) LOOP
READLINE (stddata, l); READ (l, data);
FOR j IN memory'REVERSE_RANGE(2) LOOP
memory (i,j) := data(j);
END LOOP;
END LOOP;
END PROCEDURE init_mem;
TEXTIO Based Memory init and dump Procedure

## Slide 62: Generic RAM Core
PROCEDURE dump_mem (VARIABLE memory: IN mem;
CONSTANT datafile: STRING) IS
FILE stddata : TEXT;
VARIABLE stdvalue : std_logic;
VARIABLE l : LINE;
BEGIN
FILE_OPEN (stddata, datafile, WRITE_MODE);
FOR i IN memory'RANGE(1) LOOP
FOR j IN memory'REVERSE_RANGE(2) LOOP
stdvalue := memory (i, j);
WRITE (l, stdvalue);
END LOOP;
WRITELINE (stddata, l);
END LOOP;
END PROCEDURE dump_mem;
TEXTIO Based Memory init and dump Procedure (Continued)

## Slide 63: Generic RAM Core
USE IEEE.std_logic_TEXTIO.ALL;
ENTITY std_logic_ram IS
PORT (address, datain : IN std_logic_vector;
dataout : OUT std_logic_vector;
cs, rwbar : IN std_logic; opr : IN BOOLEAN);
END ENTITY std_logic_ram;
--
ARCHITECTURE behavioral OF std_logic_ram IS
TYPE mem IS ARRAY (NATURAL RANGE <>,
NATURAL RANGE <>) of std_logic;
BEGIN
. . . . . . . . . . . . . . .
. . . . . . . . . . . . . . .
END ARCHITECTURE;
Std_logic Unconstrained Memory

## Slide 64: Generic RAM Core
PROCESS
CONSTANT memsize : INTEGER := 2**address'LENGTH;
VARIABLE memory : mem (0 TO memsize-1,
datain'RANGE);
BEGIN
id: IF opr'EVENT THEN
IF opr=TRUE THEN init_mem (memory, "memdata.dat");
ELSE dump_mem (memory, "memdump.dat"); END IF;
END IF;
wr: IF cs = '1' THEN
IF rwbar = '0' THEN -- Writing
FOR i IN dataout'RANGE LOOP
memory(conv_integer(address),i):=datain (i);
END LOOP;
. . . . . . . . . . . . . .
. . . . . . . . . . . . . .
Std_logic Unconstrained Memory (Continued)

## Slide 65: Generic RAM Core
PROCESS
CONSTANT memsize : INTEGER := 2**address'LENGTH;
VARIABLE memory : mem (0 TO memsize-1,
datain'RANGE);
BEGIN
. . . . . . . . . . . . . .
ELSE -- Reading
FOR i IN datain'RANGE LOOP
dataout(i)<=memory(conv_integer(address),i);
END LOOP;
END IF;
END IF;
WAIT ON cs, rwbar, address, datain, opr;
END PROCESS;
Std_logic Unconstrained Memory (Continued)

## Slide 66: Synthesizable Push-Pop Stack
Memory and
Queue
Structures
Generic
RAM Core
Synthesizable
Push-Pop
Stack
Synthesizable
Circular FIFO
Synthesizable
Push-Pop
Stack

## Slide 67: Synthesizable Push-Pop Stack
ENTITY stack IS
GENERIC ( max: std_logic_vector := "101111");
PORT (STin : IN std_logic_vector;
clk, push, pop : IN std_logic;
opr : IN BOOLEAN;
STout : OUT std_logic_vector;
empty, full : OUT std_logic);
END ENTITY stack;
--
Stack Controller Outline

## Slide 68: Synthesizable Push-Pop Stack
ARCHITECTURE behavioral OF stack IS
SIGNAL ramin, ramout : std_logic_vector (STin'RANGE);
SIGNAL ramaddr, pntr : std_logic_vector (max'RANGE)
:= (OTHERS => '0');
SIGNAL cs, rwbar, full_temp : std_logic:= '0';
SIGNAL empty_temp : std_logic:= '1';
BEGIN
-- UPDATING PNTR
-- POP/PUSH
-- INSTANTIATE MEMORY
-- HANDLING EMPTY AND FULL
END ARCHITECTURE behavioral;
Stack Controller Outline (Continued)

## Slide 69: Synthesizable Push-Pop Stack
-- UPDATING PNTR
Update_pntr: PROCESS (clk)
BEGIN
IF (clk = '1' AND clk'EVENT) THEN
IF pop = '1' THEN
IF empty_temp /= '1' THEN
pntr <= pntr - 1;
END IF;
ELSIF push = '1' THEN
IF full_temp /= '1' THEN
pntr <= pntr + 1;
END IF;
END IF;
END IF;
END PROCESS;
Stack Pointer Update

## Slide 70: Synthesizable Push-Pop Stack
-- POP/PUSH
pop_push: PROCESS (pop, push ,STin, ramout, pntr)
BEGIN
ramaddr <= (OTHERS => '0');
cs <= '0';
rwbar <= '1';
ramin <= (OTHERS => '0');
STout <= (STin'RANGE => '0');
IF (pop = '1' AND empty_temp = '0') THEN
ramaddr <= pntr - 1;
cs <= '1';
rwbar <= '1';
STout <= ramout;
. . .
Pop_push Process

## Slide 71: Synthesizable Push-Pop Stack
-- POP/PUSH
pop_push: PROCESS (pop, push ,STin, ramout, pntr)
BEGIN
. . . . . . . . . . . . . .
. . . . . . . . . . . . . .
ELSIF (push = '1' AND full_temp = '0') THEN
ramaddr <= pntr;
cs <= '1';
rwbar <= '0';
ramin <= STin;
END IF;
END PROCESS pop_push;
Pop_push Process (Continued)

## Slide 72: Synthesizable Push-Pop Stack
-- INSTANTIATE MEMORY
UU1: ENTITY WORK.std_logic_ram (behavioral)
PORT MAP (ramaddr, ramin, ramout, cs, rwbar, opr);
-- HANDLING EMPTY AND FULL
empty_temp <= '1' WHEN (pntr = (pntr'RANGE => '0'))
ELSE '0';
full_temp <= '1' WHEN (pntr = max) ELSE '0';
empty <= empty_temp;
full <= full_temp;
RAM Instantiation and empty and full Flags

## Slide 73: Synthesizable Circular FIFO
Memory and
Queue
Structures
Generic
RAM Core
Synthesizable
Push-Pop
Stack
Synthesizable
Circular FIFO

## Slide 74: Synthesizable Circular FIFO
Circular FIFO

## Slide 75: Synthesizable Circular FIFO
LIBRARY IEEE;
USE IEEE.std_logic_1164.ALL;
USE IEEE.std_logic_unsigned.ALL;
ENTITY fifo_unconst IS
GENERIC (fifo_size : std_logic_vector := "1000");
PORT (data_in : IN std_logic_vector;
clk : IN std_logic;
rst, rd, wr : IN std_logic;
empty, full : OUT std_logic;
data_out : OUT std_logic_vector);
END ENTITY ;
--
FIFO VHDL Code Outline

## Slide 76: Synthesizable Circular FIFO
ARCHITECTURE procedural OF fifo_unconst IS
CONSTANT fsz : INTEGER := conv_integer (fifo_size);
CONSTANT asz : INTEGER := fifo_size'LENGTH - 1;
CONSTANT wsz : INTEGER := data_in'LENGTH; --word_size;
TYPE memory IS ARRAY (NATURAL RANGE <>) OF
std_logic_vector (wsz-1 DOWNTO 0);
SIGNAL fifo_ram : memory (0 TO fsz-1);
SIGNAL rd_ptr, wr_ptr:std_logic_vector(asz-1 DOWNTO 0)
:= (OTHERS => '0');
SIGNAL full_temp, empty_temp : std_logic;
BEGIN
END ARCHITECTURE;
FIFO VHDL Code Outline (Continued)

## Slide 77: Synthesizable Circular FIFO
ARCHITECTURE procedural OF fifo_unconst IS
. . . . . . . . . . . . . .
. . . . . . . . . . . . . .
BEGIN
-- WRITE
-- READ
-- POINTER
empty_temp <= '1' WHEN ( rd_ptr=wr_ptr) ELSE '0';
full_temp <= '1' WHEN ( rd_ptr=wr_ptr + 1) ELSE '0';
empty <= empty_temp;
full <= full_temp;
END ARCHITECTURE;
FIFO VHDL Code Outline (Continued)

## Slide 78: Synthesizable Circular FIFO
FIFO Block Diagram

## Slide 79: Synthesizable Circular FIFO
Synthesizable
Circular FIFO
Clocked
Memory
Writing
Clocked
Memory
Reading
Multiple Clocked
Register
Process

## Slide 80: Clocked Memory Writing
Synthesizable
Circular FIFO
Clocked
Memory
Writing
Clocked
Memory
Reading
Multiple Clocked
Register
Process
Clocked
Memory
Writing

## Slide 81: Clocked Memory Writing
write : PROCESS (clk) BEGIN
IF (clk='1' AND clk'EVENT) THEN
IF (wr='1' AND full_temp='0') THEN
fifo_ram (conv_integer (wr_ptr)) <= data_in;
ELSIF (wr='1' AND rd='1') THEN
fifo_ram (conv_integer (wr_ptr)) <= data_in;
END IF;
END IF;
END PROCESS;
Clocked Writing: fifo_ram

## Slide 82: Clocked Memory Reading
Synthesizable
Circular FIFO
Clocked
Memory
Writing
Clocked
Memory
Reading
Multiple Clocked
Register
Process
Clocked
Memory
Reading

## Slide 83: Clocked Memory Reading
read : PROCESS (clk) BEGIN
IF (clk='1' AND clk'EVENT) THEN
IF (rd='1' AND empty_temp='0') THEN
data_out <= fifo_ram (conv_integer (rd_ptr));
ELSIF (rd='1' AND wr='1' AND empty_temp='1') THEN
data_out <= fifo_ram (conv_integer (rd_ptr));
END IF;
END IF;
END PROCESS;
Clocked Reading: fifo_ram

## Slide 84: Multiple Clocked Register Process
Synthesizable
Circular FIFO
Clocked
Memory
Writing
Clocked
Memory
Reading
Multiple Clocked
Register
Process
Multiple Clocked
Register
Process

## Slide 85: Multiple Clocked Register Process
pointer : PROCESS (clk) BEGIN
IF (clk='1' AND clk'EVENT) THEN
IF rst='1' THEN
wr_ptr <= (OTHERS => '0');
rd_ptr <= (OTHERS => '0');
ELSE
    . . . . . . . . . . . . .
    . . . . . . . . . . . . .
    . . . . . . . . . . . . .
    END IF;
END IF;
END PROCESS;
Updating FIFO Pointers

## Slide 86: Multiple Clocked Register Process
. . . . . . . . . . . . . . . .
ELSE
IF (wr='1' AND full_temp='0') OR
(wr='1' AND rd='1') THEN
wr_ptr <= wr_ptr+1;
ELSE
wr_ptr <= wr_ptr;
END IF;
IF (rd='1' AND empty_temp='0') OR
(wr='1' AND rd='1') THEN
rd_ptr <= rd_ptr+1;
ELSE
rd_ptr <= rd_ptr;
END IF;
END IF;
Updating FIFO Pointers (Continued)

## Slide 87: Arithmetic Cores
Arithmetic
Cores
Array
Multiplier
Carry
Lookahead
Adder
Synthesizable
Booth
Multiplier

## Slide 88: Array Multiplier
Arithmetic
Cores
Array
Multiplier
Carry
Lookahead
Adder
Synthesizable
Booth
Multiplier
Array
Multiplier

## Slide 89: Array Multiplier
Multiplier Cell

## Slide 90: Array Multiplier
4×4 Multiplier

## Slide 91: Array Multiplier
ENTITY bit_multiplier IS
PORT (xi, yi, pi, ci : IN std_logic;
xo, yo, po, co : OUT std_logic);
END bit_multiplier;
ARCHITECTURE logical OF bit_multiplier IS
SIGNAL xy : std_logic;
BEGIN
xy <= xi AND yi;
co <= (pi AND xy) OR (pi AND ci) OR (xy AND ci);
po <= pi XOR xy XOR ci;
xo <= xi;
yo <= yi;
END logical;
One-bit Multiplier

## Slide 92: Array Multiplier
ARCHITECTURE iterative OF array_multiplier IS
COMPONENT bit_multiplier
PORT (xi, yi, pi, ci : IN std_logic;
xo, yo, po, co : OUT std_logic);
END COMPONENT;
CONSTANT n : INTEGER := x'LENGTH - 1;
TYPE pair IS ARRAY (n+1 DOWNTO 0, n+1 DOWNTO 0) OF
std_logic;
SIGNAL xv, yv, cv, pv : pair;
BEGIN
. . . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . . .
END iterative;
Array Multiplier VHDL Description

## Slide 93: Array Multiplier
BEGIN
rows: FOR i IN x'RANGE GENERATE
cols: FOR j IN y'RANGE GENERATE
cell: bit_multiplier PORT MAP
(xv(i,j), yv(i,j), pv(i,j+1), cv(i,j),
xv(i,j+1), yv(i+1,j), pv(i+1,j), cv(i,j+1));
END GENERATE;
END GENERATE;
sides: FOR i IN x'RANGE GENERATE
xv(i, 0) <= x(i);
cv(i, 0) <= '0';
pv(0, i+1) <= '0';
pv(i+1, n+1) <= cv(i, n+1);
yv(0, i) <= y(i);
z(i) <= pv(i+1, 0);
z(i + n+1) <= pv(n+1, i+1);
END GENERATE;
END iterative;

## Slide 94: Carry-Lookahead Adder
Arithmetic
Cores
Array
Multiplier
Carry
Lookahead
Adder
Synthesizable
Booth
Multiplier
Carry
Lookahead
Adder

## Slide 95: Fast Adders
In general, any output of a 32-bit adder can be evaluated as a logic expression in terms of all 65 inputs.
Fast Adders
  Ripple carry adder
  Carry look-ahead adder
  Carry skip adder
  Carry select adder

## Slide 96: Carry Look ahead Adder
Carry look ahead logic uses the concepts of generating and propagating carries.

## Slide 97: Carry Look ahead Adders

## Slide 98: Carry Look ahead Adders
Ci+1 = xiyi+xici+ciyi
Ci+1 = xiyi+(xi+yi)ci
Generate => gi = xiyi
Propagate => pi = xi + yi
gi generate carry when it is 1
pi propagate carry when it is 1
ci+1 = gi + pici

## Slide 99: Carry Look ahead Adders

## Slide 100: Carry Expressions
ci+1 = ai  bi + ai  ci + bi  ci
si = ai  bi  ci
ci+1 = (ai + bi)  ci + ai  bi
= pi  ci + gi
pi = ai + bi
gi = ai  bi
c1 = p0  c0 + g0
c2 = p1  c1 + g1
= p1  p0  c0 + p1  g0 + g1
c3 = p2  c2 + g2 = p2  p1  p0  c0 + p2  p1  g0 + p2  g1 + g2
c4 = p3  c3 + g3
= p3  p2  p1  p0  c0 + p3  p2  p1  g0 + p3  p2  g1 + p3 
g2 + g2

## Slide 101: group propagate (PG) and group generate (GG) for an 8-bit CLA
C0
C1 = g0 + p0C0
C2 = g1 + p1C1 = g1 + p1g0 + p1p0C0
C3 = g2 + p2C2
= g2 + p2g1 + p2p1g0 + p2p1p0C0
.
.
.
C8 = g7 + p7g6 + p7p6g5 + p7p6p5g4 + p7p6p5p4g3 + p7p6p5p4p3g2 + p7p6p5p4p3p2g1 + p7p6p5p4p3p2p1g0 + p7p6p5p4p3p2p1p0C0

## Slide 102: group propagate (PG) and group generate (GG) for an 8-bit CLA
Ripple carry between blocks
Carry look ahead inside blocks

## Slide 103: group propagate (PG) and group generate (GG) for an 8-bit CLA
C8 = g7 + p7g6 + p7p6g5 + p7p6p5g4 + p7p6p5p4g3 + p7p6p5p4p3g2 + p7p6p5p4p3p2g1 + p7p6p5p4p3p2p1g0 + p7p6p5p4p3p2p1p0C0
P0 = p7p6p5p4p3p2p1p0
G0 = g7 + p7g6 + p7p6g5 + p7p6p5g4 + p7p6p5p4g3 + p7p6p5p4p3g2 + p7p6p5p4p3p2g1 + p7p6p5p4p3p2p1g0
C8 = G0 + P0C0
C16 = G1 + P1C8 = G1 + P1G0 + P1P0C0
C24 = G2 + P2G1 + P2P1G0 + P2P1P0C0
C32 = G3 + P3P2G1 + P3P2P1G0 + P3P2P1P0C0

## Slide 104: Carry-Lookahead Adder
ENTITY c_l_adder IS
PORT (a, b : IN std_logic_vector;
cin : IN std_logic;
s : OUT std_logic_vector;
cout : OUT std_logic);
END ENTITY c_l_adder;
--
A Behavioral Unconstrained Carry-lookahead Adder

## Slide 105: Carry-Lookahead Adder
ARCHITECTURE behavioral OF c_l_adder IS
SIGNAL p, g : std_logic_vector(a'RANGE);
SIGNAL carry : std_logic_vector(a'LENGTH DOWNTO 0);
BEGIN
g <= a AND b; p <= a OR b;
PROCESS (p, g, carry, cin) BEGIN
carry(0) <= cin;
FOR i IN a'REVERSE_RANGE LOOP
carry(i+1) <= g(i) OR (p(i) AND carry(i));
END LOOP;
cout <= carry(a'LENGTH);
END PROCESS;
s <= p XOR carry(a'RANGE);
END ARCHITECTURE behavioral;
A Behavioral Unconstrained Carry-lookahead Adder (Continued)

## Slide 106: Synthesizable Booth Multiplier
Arithmetic
Cores
Array
Multiplier
Carry
Lookahead
Adder
Synthesizable
Booth
Multiplier
Synthesizable
Booth
Multiplier

## Slide 107: Synthesizable Booth Multiplier
Synthesizable
Booth
Multiplier
Booth
Algorithm
Booth Multiplier
VHDL
Implementation

## Slide 108: Booth Algorithm
Synthesizable
Booth
Multiplier
Booth
Algorithm
Booth Multiplier
VHDL
Implementation
Booth
Algorithm

## Slide 109: Booth Multiplier VHDL Implementation
Synthesizable
Booth
Multiplier
Booth
Algorithm
Booth Multiplier
VHDL
Implementation
Booth Multiplier
VHDL
Implementation

## Slide 110: Booth Multiplier – VHDL
M: 0110 -M: 1010
Q: 1101
A: 0000
Appending a ‘0’ to the right of Q, and forming a 2-bit window results in:
M: 0110
Q: 1101, 0
A: 0000
Since the above window contains “10”, add –M to A, and A is shifted to the right. We also move Q window to the left to prepare it for the next cycle.
M: 0110
Q: 1101, 0
A: 1010 After add
A: 1101, 0 After shift

## Slide 111: Booth Multiplier - VHDL
Since the Q window above contains “01”, add M to A and shift. Also move the window:
M: 0110 -M: 1010
Q: 1101, 0
A: 0011, 0 After add
A: 0001, 10 After shift
Since the Q window above contains “10”, add –M to A and shift. Also move the window:
M: 0110 -M: 1010
Q: 1101, 0
A: 1011, 10 After add
A: 1101, 110 After shift

## Slide 112: Booth Multiplier VHDL Implementation
Since the above Q window contains “11”, no adding is to be done, and A is shifted to the right.
M: 0110
-M: 1010
Q: 1101, 0
A: 1110, 1110

## Slide 113: Booth Multiplier VHDL Implementation
ENTITY booth_mult IS
PORT (mc, mp : IN std_logic_vector (7 downto 0);
clk, start : IN std_logic;
prod : OUT std_logic_vector (15 downto 0);
busy : OUT boolean);
END ENTITY booth_mult;
ARCHITECTURE behavioral OF booth_mult IS
SIGNAL A, M : std_logic_vector (mc'RANGE);
SIGNAL Q : std_logic_vector (mc'LENGTH DOWNTO 0);
SIGNAL sum, dif : std_logic_vector(mc'RANGE);
SUBTYPE cnt IS INTEGER RANGE 0 TO mc'LENGTH;
SIGNAL count : cnt := 0;
BEGIN
. . . . . . . . . . . . .
END ARCHITECTURE behavioral;
Booth Algorithm VHDL Code

## Slide 114: Booth Multiplier VHDL Implementation
BEGIN
sum <= A + M;
dif <= A - M;
prod <= A & Q (mc'LENGTH DOWNTO 1);
busy <= (count < mc'LENGTH);
Counter: PROCESS (clk) BEGIN
IF (clk = '1' AND clk'EVENT) THEN
IF (start = '1') THEN count <= 0;
ELSIF (count < mc'LENGTH) THEN count<= count + 1;
END IF;
END IF;
END PROCESS;
. . . . . . . . . . . . . . . . . .
END ARCHITECTURE behavioral;
Booth Algorithm VHDL Code (Continued)

## Slide 115: Booth Multiplier VHDL Implementation
RegClocking: PROCESS (clk) BEGIN
IF (clk = '1' AND clk'EVENT) THEN
IF (start = '1') THEN
A <= (OTHERS => '0');
M <= mc;
Q <= mp & '0';
ELSIF (count < mc'LENGTH) THEN
. . . . . . . . . . . . . . .
. . . . . . . . . . . . . . .
END IF;
END IF;
END PROCESS;
Booth Algorithm VHDL Code (Continued)

## Slide 116: Booth Multiplier VHDL Implementation
. . . . . . . . . . . . . . .
ELSIF (count < mc'LENGTH) THEN
CASE Q(1 DOWNTO 0) IS
WHEN "01" => --ADD AND SHIFT
Q <= sum(0) & Q(Q'LEFT DOWNTO 1);
A <= sum(sum'LEFT) &
sum(sum'LEFT DOWNTO 1);
WHEN "10" => --SUBTRACT AND SHIFT
Q <= dif(0) & Q(Q'LEFT DOWNTO 1);
A <= dif(dif'LEFT) &
dif(dif'LEFT DOWNTO 1);
WHEN OTHERS => --SHIFT ONLY
Q <= A(0) & Q(Q'LEFT DOWNTO 1);
A <= A(A'LEFT) & A(A'LEFT DOWNTO 1);
END CASE;
END IF;
END IF;
END PROCESS;

## Slide 117: Components with Separate Control and Data Parts
Components
with Separate
Control and Data
Parts
Sequential
Multiplier
von Neumann
Computer Model

## Slide 118: Sequential Multiplier
Components
with Separate
Control and Data
Parts
Sequential
Multiplier
von Neumann
Computer Model
Sequential
Multiplier

## Slide 119: Sequential Multiplier
Multiplier Block Diagram

## Slide 120: Sequential Multiplier
Hardware Oriented Multiplication Process

## Slide 121: Sequential Multiplier
Sequential
Multiplier
Sequential
Multiplier
Design
Sequential
Multiplier
Datapath
Multiplier
Controller
Top-level
Multiplier

## Slide 122: Sequential Multiplier Design
Sequential
Multiplier
Sequential
Multiplier
Design
Sequential
Multiplier
Datapath
Multiplier
Controller
Top-level
Multiplier
Sequential
Multiplier
Design

## Slide 123: Sequential Multiplier Design
Datapath and Controller

## Slide 124: Sequential Multiplier Design
Multiplier Block Diagram

## Slide 125: Sequential Multiplier Datapath
Sequential
Multiplier
Sequential
Multiplier
Design
Sequential
Multiplier
Datapath
Multiplier
Controller
Top-level
Multiplier
Sequential
Multiplier
Datapath

## Slide 126: Sequential Multiplier Datapath
ENTITY datapath IS
PORT (clk, clr_P, load_P, load_B : IN std_logic;
msb_out, lsb_out, sel_sum : IN std_logic;
load_A, shift_A : IN std_logic;
data : INOUT std_logic_vector (7 DOWNTO 0);
A0 : OUT std_logic);
END ENTITY;
--
ARCHITECTURE procedural OF datapath IS
SIGNAL sum, ShiftAdd : std_logic_vector (7 DOWNTO 0);
SIGNAL A, B, P : std_logic_vector (7 DOWNTO 0);
SIGNAL co : std_logic;
SIGNAL op : std_logic_vector (1 DOWNTO 0);
SIGNAL result : std_logic_vector (8 DOWNTO 0);
. . . . . . . . . . . . .
END ARCHITECTURE procedural;
Shift-and-add Multiplier Datapath

## Slide 127: Sequential Multiplier Datapath
PROCESS (clk) BEGIN
IF(clk = '0' AND clk'EVENT) THEN
IF (load_B = '1') THEN B <= data;
END IF;
END IF;
END PROCESS;
--
PROCESS (clk) BEGIN
IF(clk = '0' AND clk'EVENT) THEN
IF (load_P = '1') THEN
P <= (co AND sel_sum) & ShiftAdd (7 DOWNTO 1);
END IF;
END IF;
END PROCESS;
--
Shift-and-add Multiplier Datapath (Continued)

## Slide 128: Sequential Multiplier Datapath
PROCESS (clk) BEGIN
IF(clk = '0' AND clk'EVENT) THEN
CASE op IS
WHEN "01" => A <= ShiftAdd(0) &
A(7 DOWNTO 1);
WHEN "10" => A <= data;
WHEN OTHERS => A <= A;
END CASE;
END IF;
END PROCESS;
. . . . . . . . . . . . . . . . .
Shift-and-add Multiplier Datapath (Continued)

## Slide 129: Sequential Multiplier Datapath
. . . . . . . . . . . . . .
result <= ('0'&P) + ('0'&B);
co <= result(8);
sum <= result(7 DOWNTO 0);
A0 <= A(0);
ShiftAdd <= (OTHERS => '0') WHEN clr_P = '1' ELSE
P WHEN sel_sum = '0' ELSE sum;
data <= A WHEN lsb_out = '1' ELSE (OTHERS => 'Z');
data <= P WHEN msb_out = '1' ELSE (OTHERS => 'Z');
op <= load_A & shift_A;
END ARCHITECTURE procedural;
Shift-and-add Multiplier Datapath (Continued)

## Slide 130: Multiplier Controller
Sequential
Multiplier
Sequential
Multiplier
Design
Sequential
Multiplier
Datapath
Multiplier
Controller
Top-level
Multiplier
Multiplier
Controller

## Slide 131: Multiplier Controller
LIBRARY IEEE;
USE IEEE.std_logic_1164.ALL;
USE IEEE.std_logic_unsigned.ALL;
ENTITY controller IS
PORT (clk, start, A0 : IN std_logic;
clr_P, load_P, load_B : OUT std_logic;
msb_out, lsb_out, sel_sum : OUT std_logic;
load_A, Shift_A, done : OUT std_logic);
END ENTITY;
--
Multiplier Controller

## Slide 132: Multiplier Controller
ARCHITECTURE procedural OF controller IS
TYPE state IS (idle, init,
m1, m2, m3, m4, m5, m6, m7, m8,
rslt1, rslt2);
SIGNAL current : state;
BEGIN
sequential: PROCESS (clk) BEGIN
IF (clk = '0' AND clk'EVENT) THEN
CASE current IS
WHEN idle =>
IF start = '0' THEN current <= idle;
ELSE
current <= init;
END IF;
. . . . . . . . . . . . . .
END PROCESS; --
Multiplier Controller (Continued)

## Slide 133: Multiplier Controller
sequential: PROCESS (clk) BEGIN
IF (clk = '0' AND clk'EVENT) THEN
CASE current IS
. . . . . . . . . . . . . . .
WHEN init =>
current <= m1;
WHEN m1 | m2 | m3 | m4 | m5 | m6 | m7 | m8 =>
current <= state'SUCC(current);
WHEN rslt1 =>
current <= rslt2;
WHEN rslt2 =>
current <= idle;
WHEN OTHERS =>
current <= idle;
END CASE;
Multiplier Controller

## Slide 134: Multiplier Controller
sequential: PROCESS (clk) BEGIN
. . . . . . . . . . . . . . .
END PROCESS; --
combinational: PROCESS (current, start, A0) BEGIN
clr_P <= '0'; load_P <= '0';
load_B <= '0';
msb_out <= '0'; lsb_out <= '0';
sel_sum <= '0'; load_A <= '0';
Shift_A <= '0'; done <= '0';
CASE current IS
WHEN idle =>
IF start = '0' THEN
done <= '1';
ELSE
load_A <= '1';
clr_P<= '1';
load_P <= '1';
END IF;

## Slide 135: Multiplier Controller
combinational: PROCESS (current, start, A0) BEGIN
CASE current IS
. . . . . . . . . . . . . . . .
WHEN init =>
load_B <= '1';
WHEN m1 | m2 | m3 | m4 | m5 | m6 | m7 | m8 =>
Shift_A <= '1';
load_P <= '1';
IF (A0 = '1') THEN
sel_sum <= '1';
END IF;
WHEN rslt1 =>
lsb_out <= '1';
WHEN rslt2 =>
msb_out <= '1';
Multiplier Controller

## Slide 136: Multiplier Controller
combinational: PROCESS (current, start, A0) BEGIN
CASE current IS
. . . . . . . . . . . . . . . .
WHEN rslt2 =>
msb_out <= '1';
WHEN OTHERS =>
clr_P <= '0'; load_P <= '0';
load_B <= '0'; msb_out <= '0';
lsb_out <= '0'; sel_sum <= '0';
load_A <= '0'; Shift_A <= '0';
done <= '0';
END CASE;
END PROCESS;
END ARCHITECTURE procedural;
Multiplier Controller

## Slide 137: Top-level Multiplier
Sequential
Multiplier
Sequential
Multiplier
Design
Sequential
Multiplier
Datapath
Multiplier
Controller
Top-level
Multiplier
Top-Level
Multiplier

## Slide 138: Top-level Multiplier
ENTITY Multiplier IS
PORT (clk, start : IN std_logic;
databus : INOUT std_logic_vector (7 DOWNTO 0);
lsb_out, msb_out, done : OUT std_logic);
END ENTITY;
--
ARCHITECTURE structural OF Multiplier IS
SIGNAL clr_P, load_P, load_B, msb_out_t, A0 : std_logic;
SIGNAL lsb_out_t, sel_sum, load_A, Shift_A : std_logic;
BEGIN
. . . . . . . . . . . . .
. . . . . . . . . . . . .
END ARCHITECTURE structural;
Top-level Multiplier Module

## Slide 139: Top-level Multiplier
ARCHITECTURE structural OF Multiplier IS
BEGIN
dpu : ENTITY WORK.datapath(procedural)
PORT MAP (clk, clr_P, load_P, load_B,
msb_out_t, lsb_out_t, sel_sum,
load_A, Shift_A, databus, A0 );
cu : ENTITY WORK.controller(procedural)
PORT MAP (clk, start, A0, clr_P, load_P, load_B,
msb_out_t, lsb_out_t, sel_sum,
load_A, Shift_A, done );
msb_out <= msb_out_t;
lsb_out <= lsb_out_t;
END ARCHITECTURE structural;
Top-level Multiplier Module (Continued)

## Slide 140: von Neumann Computer Model
Components
with Separate
Control and Data
Parts
Sequential
Multiplier
von Neumann
Computer Model
von Neumann
Computer Model

## Slide 141: von Neumann Computer Model
von Neumann
Computer Model
Processor and
Memory Model
Processor Model
Specification
Designing the
Adding CPU
Design of Datapath
Control Part Design
AddingCPU
VHDL Description
Data Components
DataPath Description
Controller Description
The Complete Machine

## Slide 142: Processor and Memory Model
von Neumann
Computer Model
Processor and
Memory Model
Processor Model
Specification
Designing the
Adding CPU
Design of Datapath
Control Part Design
AddingCPU
VHDL Description
Data Components
DataPath Description
Controller Description
The Complete Machine
Processor and
Memory Model

## Slide 143: Processor and Memory Model
von Neumann Process Model

## Slide 144: Processor Model Specification
von Neumann
Computer Model
Processor and
Memory Model
Processor Model
Specification
Designing the
Adding CPU
Design of Datapath
Control Part Design
AddingCPU
VHDL Description
Data Components
DataPath Description
Controller Description
The Complete Machine
Processor Model
Specification

## Slide 145: Processor Model Specification
Interface of the Adding CPU

## Slide 146: Processor Model Specification
Instruction Format

## Slide 147: Designing the Adding CPU
von Neumann
Computer Model
Processor and
Memory Model
Processor Model
Specification
Designing the
Adding CPU
Design of Datapath
Control Part Design
AddingCPU
VHDL Description
Data Components
DataPath Description
Controller Description
The Complete Machine
Designing the
Adding CPU

## Slide 148: Design of Datapath
von Neumann
Computer Model
Processor and
Memory Model
Processor Model
Specification
Designing the
Adding CPU
Design of Datapath
Control Part Design
AddingCPU
VHDL Description
Data Components
DataPath Description
Controller Description
The Complete Machine
Design of Datapath

## Slide 149: Design of Datapath
Architectural Design of our Adding Machine

## Slide 150: Control Part Design
von Neumann
Computer Model
Processor and
Memory Model
Processor Model
Specification
Designing the
Adding CPU
Design of Datapath
Control Part Design
AddingCPU
VHDL Description
Data Components
DataPath Description
Controller Description
The Complete Machine
Control Part Design

## Slide 151: Control Part Design
Controller of Adding CPU

## Slide 152: AddingCPU VHDL Description
von Neumann
Computer Model
Processor and
Memory Model
Processor Model
Specification
Designing the
Adding CPU
Design of Datapath
Control Part Design
AddingCPU
VHDL Description
Data Components
DataPath Description
Controller Description
The Complete Machine
AddingCPU
VHDL Description

## Slide 153: Data Components
von Neumann
Computer Model
Processor and
Memory Model
Processor Model
Specification
Designing the
Adding CPU
Design of Datapath
Control Part Design
AddingCPU
VHDL Description
Data Components
DataPath Description
Controller Description
The Complete Machine
Data Components

## Slide 154: Data Components
ENTITY AC IS
PORT (data_in : IN std_logic_vector(7 DOWNTO 0);
load, clk : IN std_logic;
data_out : OUT std_logic_vector(7 DOWNTO 0));
END ENTITY ;
--
ARCHITECTURE procedural OF AC IS BEGIN
PROCESS (clk) BEGIN
IF clk = '1' AND clk'EVENT THEN
IF load = '1' THEN
data_out <= data_in;
END IF;
END IF;
END PROCESS;
END ARCHITECTURE;
Datapath Components of the Adding Machine

## Slide 155: Data Components
ENTITY IR IS
PORT (data_in : IN std_logic_vector(7 DOWNTO 0);
load, clk : IN std_logic;
data_out : OUT std_logic_vector(7 DOWNTO 0));
END ENTITY ;
--
ARCHITECTURE procedural OF IR IS BEGIN
PROCESS (clk) BEGIN
IF clk = '1' AND clk'EVENT THEN
IF load = '1' THEN data_out <= data_in; END IF;
END IF;
END PROCESS;
END ARCHITECTURE;
Datapath Components of the Adding Machine (Continued)

## Slide 156: Data Components
ENTITY PC IS
PORT (data_in : IN std_logic_vector(5 DOWNTO 0);
load, inc, clr, clk : IN std_logic;
data_out : OUT std_logic_vector(5 DOWNTO 0));
END ENTITY ;
ARCHITECTURE procedural OF PC IS
SIGNAL pc : std_logic_vector(5 DOWNTO 0);
BEGIN
PROCESS (clk) BEGIN
IF clk = '1' AND clk'EVENT THEN
IF clr = '1' THEN pc <= (OTHERS => '0');
ELSIF load = '1' THEN pc <= data_in;
ELSIF inc = '1' THEN pc <= pc + 1; END IF;
END IF;
END PROCESS;
data_out <= pc;
END ARCHITECTURE;

## Slide 157: Data Components
ENTITY ALU IS
PORT (a, b : IN std_logic_vector(7 DOWNTO 0);
pass, add : IN std_logic;
alu_out : OUT std_logic_vector(7 DOWNTO 0));
END ENTITY ;
ARCHITECTURE functional OF ALU IS
SIGNAL alu_res : std_logic_vector(7 DOWNTO 0);
BEGIN
PROCESS (a, b, pass, add) BEGIN
IF pass = '1' THEN alu_res <= a;
ELSIF add = '1' THEN alu_res <= a + b;
ELSE alu_res <= (OTHERS => '0');
END IF;
END PROCESS;
alu_out <= alu_res;
END ARCHITECTURE;
Datapath Components of the Adding Machine (Continued)

## Slide 158: DataPath Description
von Neumann
Computer Model
Processor and
Memory Model
Processor Model
Specification
Designing the
Adding CPU
Design of Datapath
Control Part Design
AddingCPU
VHDL Description
Data Components
DataPath Description
Controller Description
The Complete Machine
DataPath Description

## Slide 159: DataPath Description
ENTITY datapath IS
PORT (ir_on_adr, pc_on_adr, dbus_on_data : IN std_logic;
data_on_dbus, ld_ir, ld_ac, ld_pc : IN std_logic;
inc_pc, clr_pc,
pass, add, alu_on_dbus, clk : IN std_logic;
adr_bus : OUT std_logic_vector(5 DOWNTO 0);
op_code : OUT std_logic_vector(1 DOWNTO 0);
data_bus : INOUT std_logic_vector(7 DOWNTO 0));
END ENTITY ;
ARCHITECTURE structural OF datapath IS
SIGNAL dbus, ir_out, a_side :
std_logic_vector(7 DOWNTO 0);
SIGNAL alu_out, b_side : std_logic_vector(7 DOWNTO 0);
SIGNAL pc_out : std_logic_vector(5 DOWNTO 0);
. . . . . . . . . . . . . . . .
END ARCHITECTURE;
Adding CPU Datapath Description

## Slide 160: DataPath Description
ARCHITECTURE structural OF datapath IS
BEGIN
IR : ENTITY WORK.IR(procedural)
PORT MAP (dbus, ld_ir, clk, ir_out);
PC : ENTITY WORK.PC(procedural)
PORT MAP (ir_out(5 DOWNTO 0), ld_pc, inc_pc,
clr_pc, clk, pc_out);
AC : ENTITY WORK.AC(procedural)
PORT MAP (dbus, ld_ac, clk, a_side);
ALU : ENTITY WORK.ALU(functional)
PORT MAP (a_side, b_side, pass, add, alu_out );
b_side <= '0'&'0'&ir_out(5 DOWNTO 0);
. . . . . . . . . . . . . . . . . . .
END ARCHITECTURE;
Adding CPU Datapath Description (Continued)

## Slide 161: DataPath Description
ARCHITECTURE structural OF datapath IS
BEGIN
. . . . . . . . . . . . . . . . .
adr_bus <= ir_out(5 DOWNTO 0) WHEN ir_on_adr = '1' ELSE (OTHERS => 'Z');
adr_bus <= pc_out WHEN pc_on_adr = '1' ELSE
(OTHERS => 'Z');
dbus <= alu_out WHEN alu_on_dbus = '1' ELSE
(OTHERS => 'Z');
data_bus <= dbus WHEN dbus_on_data = '1' ELSE
(OTHERS => 'Z');
dbus <= data_bus WHEN data_on_dbus = '1' ELSE
(OTHERS => 'Z');
op_code <= ir_out(7 DOWNTO 6);
END ARCHITECTURE;
Adding CPU Datapath Description (Continued)

## Slide 162: Controller Description
von Neumann
Computer Model
Processor and
Memory Model
Processor Model
Specification
Designing the
Adding CPU
Design of Datapath
Control Part Design
AddingCPU
VHDL Description
Data Components
DataPath Description
Controller Description
The Complete Machine
Controller Description

## Slide 163: Controller Description
ENTITY controller IS
PORT (rst, clk : IN std_logic;
op_code : IN std_logic_vector(1 DOWNTO 0);
rd_mem, wr_mem : OUT std_logic;
ir_on_adr, pc_on_adr : OUT std_logic;
dbus_on_data, data_on_dbus, ld_ir : OUT std_logic;
ld_ac, ld_pc, inc_pc, clr_pc,pass : OUT std_logic;
add, alu_on_dbus : OUT std_logic);
END ENTITY ;
--
ARCHITECTURE procedural OF controller IS
TYPE state IS (Reset, Fetch, Decode, Execute);
SIGNAL present_state, next_state : state;
BEGIN
. . . . . . . . . . . . . . . . . .
END ARCHITECTURE;
Controller VHDL Code

## Slide 164: Controller Description
ARCHITECTURE procedural OF controller IS
BEGIN
PROCESS (clk)--Sequential
BEGIN
IF clk = '1' AND clk'EVENT THEN
IF rst = '1' THEN
present_state <= Reset;
ELSE
present_state <= next_state;
END IF;
END IF;
END PROCESS;
--
. . . . . . . . . . . . . . . .
END ARCHITECTURE;
Controller VHDL Code (Continued)

## Slide 165: Controller Description
PROCESS (present_state, rst) --Combinational
BEGIN
rd_mem <= '0'; wr_mem <= '0'; ir_on_adr <= '0';
pc_on_adr <= '0'; dbus_on_data <= '0';
data_on_dbus <= '0'; ld_ir <= '0'; pass <= '0';
ld_ac <= '0'; ld_pc <= '0'; inc_pc <= '0';
clr_pc <= '0'; add <= '0'; alu_on_dbus <= '0';
CASE present_state IS
WHEN Reset =>
IF rst = '1' THEN
next_state <= Reset;
ELSE
next_state <= Fetch;
END IF;
clr_pc <= '1';
. . . . . . . . . . . . . . .
Controller VHDL Code (Continued)

## Slide 166: Controller Description
PROCESS (present_state, rst, op_code) --Combinational
BEGIN
. . . . . . . . . . . . . . . .
WHEN Fetch =>
next_state <= Decode;
pc_on_adr <= '1';
rd_mem <= '1';
data_on_dbus <= '1';
ld_ir <= '1';
inc_pc <= '1';
WHEN Decode =>
next_state <= Execute;
. . . . . . . . . . . . . . . .
END PROCESS;
. . . . . . . . . . . . . . .
Controller VHDL Code (Continued)

## Slide 167: Controller Description
. . . . . . . . . . . . . . . .
WHEN Execute =>
next_state <= Fetch;
CASE op_code IS
WHEN "00" =>
ir_on_adr <= '1'; rd_mem <= '1';
data_on_dbus <= '1'; ld_ac <= '1';
WHEN "01" =>
dbus_on_data <= '1';alu_on_dbus<= '1';
pass <= '1'; wr_mem <= '1';
ir_on_adr <= '1';
WHEN "10" =>
ld_pc <= '1';
WHEN "11" =>
add <= '1'; alu_on_dbus <= '1';
ld_ac <= '1';
Controller VHDL Code

## Slide 168: Controller Description
. . . . . . . . . . . . . . . .
WHEN OTHERS =>
rd_mem <= '0'; pc_on_adr <= '0';
pass <= '0';
ir_on_adr <= '0'; wr_mem <= '0';
ld_ac <= '0';
dbus_on_data <= '0';data_on_dbus<='0';
ld_ir <= '0'; alu_on_dbus <= '0';
add <= '0';
inc_pc <= '0'; clr_pc <= '0';
ld_pc <= '0';
END CASE;
WHEN OTHERS => next_state <= Reset;
END CASE;
END PROCESS;
END ARCHITECTURE;
Controller VHDL Code

## Slide 169: The Complete Machine
von Neumann
Computer Model
Processor and
Memory Model
Processor Model
Specification
Designing the
Adding CPU
Design of Datapath
Control Part Design
AddingCPU
VHDL Description
Data Components
DataPath Description
Controller Description
The Complete Machine
The Complete Machine

## Slide 170: The Complete Machine
ENTITY addingCPU IS
PORT (reset, clk : IN std_logic;
adr_bus : OUT std_logic_vector(5 DOWNTO 0);
rd_mem, wr_mem : OUT std_logic;
data_bus : INOUT std_logic_vector(7 DOWNTO 0));
END ENTITY ;
--
ARCHITECTURE structural OF addingCPU IS
SIGNAL ir_on_adr, pc_on_adr, dbus_on_data : std_logic;
SIGNAL data_on_dbus, ld_ir, ld_ac, ld_pc : std_logic;
SIGNAL inc_pc, clr_pc : std_logic;
SIGNAL pass, add, alu_on_dbus : std_logic;
SIGNAL op_code : std_logic_vector(1 DOWNTO 0);
BEGIN
. . . . . . . . . . . . . . . .
END ARCHITECTURE;
AddingCPU Top-level Description

## Slide 171: The Complete Machine
ARCHITECTURE structural OF addingCPU IS
BEGIN
CU: ENTITY WORK.Controller
PORT MAP (reset, clk, op_code, rd_mem,
wr_mem, ir_on_adr, pc_on_adr,
dbus_on_data, data_on_dbus,
ld_ir, ld_ac, ld_pc, inc_pc,
clr_pc, pass, add, alu_on_dbus );
DP: ENTITY WORK.DataPath
PORT MAP (ir_on_adr, pc_on_adr, dbus_on_data,
data_on_dbus,ld_ir, ld_ac, ld_pc,
inc_pc, clr_pc, pass, add,
alu_on_dbus, clk, adr_bus, op_code,
data_bus );
END ARCHITECTURE;
AddingCPU Top-level Description (Continued)

## Slide 172: Summary
This chapter presented VHDL code and descriptions for several hardware components.
Emphasized on synthesizable cores
Considered situations that a core model was to be for evaluation purposes only
We discussed:
  Individual stand-alone component descriptions
  Design partitioning
  Putting sub-components of a system together for formation of complete systems.

## Slide 173: Acknowledgment
Last Revision by: Hanieh Hashemi.